## Slide 1: Building Materials-I
BARCH408-21
Aluminium as a building material

## Slide 2: Classification of Aluminium
Aluminium as a building material can be classified into various categories based on its form, application, and characteristics. Here are some common classifications:
Aluminium Alloys:
Different alloys of aluminium are used for specific applications. Common alloy series, each with distinct properties suitable for various structural and non-structural components.

## Slide 3
Architectural Aluminium:
  This category includes aluminium used in architectural elements like window frames, doors, curtain walls, and façade systems. Architectural aluminium is often characterized by its aesthetics, durability, and suitability for design versatility.
Structural Aluminium:
  Aluminium is utilized in structural applications such as beams, columns, and trusses. High-strength alloys, are commonly employed for structural purposes.
Extruded Aluminium:
  Extruded aluminium profiles are created by shaping aluminium through an extrusion process. This category includes a wide range of profiles used in construction, such as beams, channels, and frames.

## Slide 4
Rolled Aluminium:
  Rolled aluminium products are formed by passing aluminium through rollers. Sheets and plates are common forms of rolled aluminium used in roofing, cladding, and structural applications.
Aluminium Composite Materials (ACM):
  ACM consists of a core material sandwiched between two layers of aluminium sheets. These materials are used in architectural cladding, signage, and decorative applications.
Anodized Aluminium:
  Anodizing is an electrochemical process that forms a durable oxide layer on the surface of aluminium . Anodized aluminium is corrosion-resistant and often used for architectural finishes, creating a range of colors and textures.

## Slide 5
Powder-Coated Aluminium:
  Powder coating is a finishing process where a dry powder is applied to Aluminium surfaces and cured to form a protective layer. Powder-coated Aluminium is used for architectural elements and offers enhanced durability and color options.
Aluminium in Roofing:
  Aluminium roofing materials, such as standing seam panels, are lightweight, corrosion-resistant, and widely used for residential and commercial roofing applications.
Aluminium Windows and Doors:
  Aluminium is commonly used in the manufacturing of window frames and doors due to its strength, durability, and ability to accommodate large spans.

## Slide 6: Properties of Aluminium
Aluminium possesses several notable properties that make it a valuable and widely used material in various applications. Here are some key properties of aluminium:
Lightweight
Corrosion Resistance
High Strength-to-Weight Ratio
Ductility
Conductivity

## Slide 7
Thermal Conductivity
Non-Magnetic
Reflectivity
Recyclability
Malleability
Resilience
Non-Toxic

## Slide 8: Characteristics of Aluminium
1. Lightweight
2. Corrosion-resistant
3. High strength-to-weight ratio
4. Ductile
5. Good electrical conductivity
6. Excellent thermal conductivity
7. Non-magnetic
8. Reflective
9. Recyclable
10. Malleable
11. Resilient
12. Non-toxic

## Slide 9: Uses of Aluminium
1. Aerospace industry
2. Construction materials
3. Electrical transmission lines
4. Heat exchangers
5. Cooking utensils
6. Automotive components
7. Packaging materials
8. Reflective coatings
9. Mirrors
10. Solar reflectors
11. Structural components
12. Aluminium foil and containers

## Slide 10: Types of Aluminium's
Pure Aluminium (1000 Series):
  Highly ductile and corrosion-resistant.
  Used in electrical conductors, cooking utensils, and chemical processing.
Aluminium Alloys (2000 Series):
  High strength and excellent machinability.
  Commonly used in aerospace applications and structural components.
Aluminium -Manganese Alloys (3000 Series):
  Improved corrosion resistance.
  Used in applications like cooking utensils and chemical equipment.

## Slide 11
Aluminium-Silicon Alloys (4000 Series):
  Good fluidity in casting.
  Used in welding filler materials and automotive components.
Aluminium-Magnesium Alloys (5000 Series):
  High strength and excellent corrosion resistance.
  Commonly used in marine applications, vehicle bodies, and structural components.
Aluminium-Magnesium-Silicon Alloys (6000 Series):
  Good combination of strength and formability.
  Widely used in architectural extrusions, automotive parts, and structural components.

## Slide 12
Aluminium-Zinc Alloys (7000 Series):
  High strength and toughness.
  Used in aerospace applications and high-stress structural components.
Aluminium-Lithium Alloys:
  Lightweight with enhanced stiffness.
  Used in aerospace and aircraft manufacturing for weight reduction.
Wrought Aluminium-Titanium Alloys (7000 Series):
  High strength and good toughness.
  Applied in aerospace and high-performance structural applications.

## Slide 13
Cast Aluminium Alloys (8000 Series):
  Designed for casting processes.
  Used in automotive parts, machinery components, and general casting applications.
These are just some examples, and there are many other aluminium alloys with specific compositions tailored for different purposes. The alloying elements influence properties such as strength, corrosion resistance, machinability, and formability, allowing for a wide range of applications across various industries.

## Slide 14: Applications of Aluminium in buildings
Windows and Window Frames:
Doors and Door Frames:
Curtain Walls:
Roofing Systems:
Cladding and Facades:
Structural Components:
Architectural Extrusions:
Balustrades and Railings:
Skylights and Canopies:
Interior Partitions:
Suspended Ceilings:
Solar Shading Systems: