## Slide 1: Dampness and Damp Proofing
Building Construction Practice

## Slide 2: Dampness
Dampness refers to the presence of excess moisture in the walls, floors, or ceilings of a building, which can weaken the structure and create an unhealthy environment.

## Slide 3: Possible Causes of Dampness
Capillary Action: Water rises from the ground through foundation walls due to capillary action.
Rainwater Penetration: Poor roofing, cracked walls, or faulty external plaster allow rainwater to seep in.
Leakage from Pipes: Faulty plumbing, leaking water supply pipes, or drainage issues contribute to dampness.
Condensation: Excess moisture in the air condenses on walls and ceilings, especially in humid conditions.
Poor Drainage System: Improper slope or lack of drainage around the building leads to water accumulation.
Defective Damp-Proof Course (DPC): Absence or failure of damp-proofing layers allows moisture ingress.

## Slide 4: Ill Effects of Dampness
Weakens Structure: Moisture reduces the strength of walls, floors, and roofs, leading to cracks and decay.
Promotes Mold Growth: Favors the growth of fungus, mold, and mildew, causing health issues.
Damages Paint & Plaster: Leads to peeling paint, flaking plaster, and salt deposits (efflorescence).
Unhealthy Living Conditions: Causes bad odors, damp air, and respiratory problems.
Corrosion of Metal Fixtures: Moisture leads to rusting of steel reinforcements and metal parts.

## Slide 5: Ill Effects of Dampness
Weakens Structure: Moisture reduces the strength of walls, floors, and roofs, leading to cracks and decay.
Promotes Mold Growth: Favors the growth of fungus, mold, and mildew, causing health issues.
Damages Paint & Plaster: Leads to peeling paint, flaking plaster, and salt deposits (efflorescence).
Unhealthy Living Conditions: Causes bad odors, damp air, and respiratory problems.
Corrosion of Metal Fixtures: Moisture leads to rusting of steel reinforcements and metal parts.

## Slide 6: Methods of Preventing Dampness in Buildings
1. Damp-Proof Course (DPC)
  A continuous layer of waterproof material (bitumen, cement concrete, metal sheets, etc.) is provided at plinth level, walls, and floors.
  Prevents capillary rise of water from the ground.
2. Integral Damp-Proofing
  Waterproofing compounds (like sodium silicate, aluminum sulfate, or calcium chloride) are mixed with cement to improve resistance to moisture.
  Used in concrete foundations, basements, and floors.

## Slide 7
3. Surface Treatment
  Waterproof coatings (such as bitumen, cement plaster with water-repellent additives, or special paints) are applied to walls, roofs, and floors.
  Prevents rainwater penetration and enhances moisture resistance.
4. Cavity Wall Construction
  A hollow space (cavity) is left between two brick walls, preventing external moisture from reaching the inner wall.
  Common in high-rainfall areas.
5. Guniting (Cement Mortar Spraying)
  A high-pressure spray of rich cement mortar (1:3 ratio) is applied on damp walls or damaged surfaces.
  Used for repairing old buildings and strengthening weak walls.

## Slide 8
6. Proper Drainage System
  Ensuring efficient drainage around the building prevents water accumulation near foundations.
  Includes proper ground slopes, surface drains, and rainwater gutters.
7. Ventilation and Dehumidification
  Providing adequate ventilation, cross-ventilation, and exhaust fans helps reduce indoor humidity.
  Dehumidifiers can be used in humid regions to control moisture levels.

## Slide 9: Dam-proof Materials
1. Flexible Materials
  Bituminous Coatings (Asphalt, Bitumen Felt): Used as a waterproof layer in DPC courses, walls, and roofs.
  Polymer-Based Waterproof Membranes: Includes PVC sheets and rubberized asphalt, ideal for roofs and basements.
2. Rigid Materials
  Cement Concrete (1:2:4 mix): Used as a DPC layer at plinth level.
  Bricks & Stones: Used in thick masonry walls to resist dampness.

## Slide 10
3. Semi-Rigid Materials
  Mastic Asphalt: A mixture of bitumen and sand, applied in roofing, basements, and floors.
  Metal Sheets (Lead, Copper, Aluminum): Used in foundations and damp courses for high moisture resistance.
4. Integral Waterproofing Compounds
  Added to cement mortar to increase water resistance.
  Examples: Sodium Silicate, Calcium Chloride, Aluminum Sulphate.

## Slide 11
5. Chemical Damp-Proofing Agents
  Silicone-Based Water Repellents: Used as surface coatings on walls.
  Epoxy Resins & Acrylic Coatings: Used for flooring, basements, and swimming pools.

## Slide 12: Principles pertaining to the use of dam-proof materials
1. Selection of Suitable Damp-Proofing Material
  Choose materials based on climatic conditions, building type, and location (e.g., bitumen for roofs, metal sheets for foundations).
  Materials should be water-resistant, durable, and compatible with the building structure.
2. Proper Thickness and Placement
  Damp-proof course (DPC) layers should have a minimum thickness of 2-5 cm, depending on the material.
  It must be placed at appropriate locations, such as plinth level, basement floors, and roofs.

## Slide 13
3. Continuous Damp-Proofing Layer
  The damp-proof layer should be unbroken across the entire surface to prevent moisture penetration.
  Joints must be properly sealed using overlapping techniques or adhesives.
4. Effective Surface Preparation
  The surface should be clean, level, and free from dust or cracks before applying damp-proofing materials.
  Primer coats or bonding agents should be used for better adhesion.

## Slide 14
5. Proper Drainage and Ventilation
  Good drainage systems (e.g., sloped surfaces, rainwater pipes) should be provided to direct water away from buildings.
  Proper ventilation in walls and basements prevents condensation and moisture buildup.
6. Prevention of Capillary Action
  Materials like concrete, bitumen, and metal sheets should be used at the foundation level to stop moisture from rising.
  Cavity walls can be introduced to create air gaps for extra protection.

## Slide 15
7. Maintenance and Repair
  Regular inspection and maintenance of damp-proofing layers to fix cracks or leaks.
  Reapplication of waterproof coatings if necessary, especially in exposed areas.